Risk Assessment

Activity Assessed: Working at height above or near a suspended ceiling             Assessment Date: 01.02.2019	Assessment Reference: (v1)

Name of Assessor: G. Pinder	                Review Date: February 2021

| Ref. No. | Hazard | Persons at Risk and How They Might be Harmed | Controls Currently in Place | Current Risk Level | Further Controls Recommended | Action by Whom | Action by Date | Completed Date |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
|  |  |  |  | L | S | T | Risk Rating |  |  |  |  |
| 1 | Fall off ladders | Engineer |  |  |  |  |  |  |  |  |  |
|  |  |  | Training provided on the safe use of ladders. | 2 | 2 | 4 | Medium |  |  |  |  |
| 2 | Ladders or steps collapsing | Engineer | Engineer is trained to examine steps and ladders for defects prior to each use. |  |  |  |  |  |  |  |  |
|  |  |  | A supervisor inspects ladders and steps at least bi-annually and records the results. | 1 | 2 | 2 | Low |  |  |  |  |
| 3 | Fall from a work platform | Engineer | Any work platform must be of a substantial material, i.e. non fragile with a permanent perimeter guard rail. | 1 | 2 | 2 | Low |  |  |  |  |
| 4 | Low level lighting | Engineer | Engineer to report to customer where lighting levels are low. Two man operation when the problem persists. | 1 | 1 | 1 | Low |  |  |  |  |
| 5 | Safe access | Engineer | The engineer uses the ladder provided and ensures it is hooked correctly over the hook provided. | 1 | 2 | 2 | Low |  |  |  |  |
| 6 | Manual lifting | Engineer | Engineer is trained in manual handling techniques. Lift truck, sack barrows etc. Available where necessary. For jobs including difficult manual handling, engineer and others to discuss beforehand and agree a safe system of work. | 1 | 2 | 2 | Low |  |  |  |  |
| 7 | Slips, trips and falls | Engineer, client’s staff and the public | Warning signs in noticeable areas. Spillage procedure in place for clearing standing liquids. No storage of materials or waste in public walkways. Trailing lead distance kept to a minimum by utilising nearest electrical point. Areas segregated or closed off where wet cleaning is undertaken. | 1 | 2 | 2 | Low |  |  |  |  |
| 8 | Fall through the adjacent suspended ceiling | Engineer and persons working underneath | The engineer does not climb over the guard rail. Provision of a physical barrier; should be 950mm high with middle bar protection (no gap more than 470mm) and toe board. No work within 2 metres of the ceiling if unprotected. The safe working area is marked/designated. Safety harnesses used where necessary. No stepping on a false ceiling. Work not commenced until adequate arrangements put in place. | 2 | 2 | 4 | Medium |  |  |  |  |

SIGN OFF / REVIEW:

Changes arising from the review process will be highlighted by text colouring as indicated at the review sign off section (eg. 2017 Changes).

Date:				Name:	 				Position: 				Signature:

Date:				Name:					Position:				Signature:

Date:				Name:					Position:				Signature:

Date:				Name:					Position:				Signature:

Date:				Name:					Position:				Signature:

Risk Assessment Information

Risk Rating Key:

| Risk Level | Description |
| --- | --- |
| Low | No additional controls are required unless they can be implemented at very low cost (in terms of time, money and effort). Actions to further reduce these risks are assigned low priority. Arrangements should be made to ensure that the controls are maintained. |
| Medium | Consideration should be given as to whether the risks can be lowered, but the costs of additional risk reduction measures should be taken into account. The risk reduction measures should be implemented within a defined time period. Arrangements should be made to ensure that the controls are maintained, particularly if the risk levels are associated with harmful consequences. |
| High | Substantial efforts should be made to reduce the risk. Risk reduction measures should be implemented urgently within a defined time period and it might be necessary to consider suspending or restricting the activity, or to apply interim risk controls, until this has been completed. Considerable resources might have to be allocated to additional controls. Arrangements should be made to ensure that the controls are maintained, particularly if the risk levels are associated with extremely harmful consequences and very harmful consequences. |

Definitions:

| Risk Assessment | A systematic examination of workplace risks in 5 steps: 1) Identify the hazards, 2) Identify who might be harmed and how, 3) Evaluation the hazard (by examining current controls and recommending further controls), 4) Recording the assessment and 5) Reviewing the assessment. |
| --- | --- |
| Hazard | Something with the potential to cause harm e.g. tools, machinery, work equipment, substances, workstation, unsafe system of work etc. |
| Harm | The damage that a hazard may cause e.g. physiological effects (physical injury, ill health) and psychological factors (e.g. stress), loss of time/efficiency and damage to the premises/equipment. |
| Likelihood | The chance that a hazard realises its potential to cause harm. |
| Severity | Extent of injury, damage etc. |
| Risk | The probability of a hazard actually causing harm. |
| Controls | Measures introduced or installed to reduce to a minimum the possibility of harm to persons, plant and property. |

Confirmation of Staff Training in Risk Assessment:

Having examined this risk assessment, please sign below to confirm that you have read this and understand the content and the control measures which are detailed. If you have any questions on the content, sign only after you have received a full explanation from your Manager.

| Name (BLOCK CAPITALS) | Signature | Date |
| --- | --- | --- |

| Risk Rating Meaning | 7-9 : High | 4-6 : Medium | 1 : 3 Low |
| --- | --- | --- | --- |
| Pre Control Risk Calculation |
| a) Potential Injury | Score Rating | b) Likelihood of Exposure | Score Rating | Risk = Potential Injury x Likelihood of exposure |
|  |  |  |  |  | Score |
| Severe (Fatal) | 3 | Likely | 3 | a - Potential Injury |  |
| Moderate | 2 | Unlikely | 2 | b - Likelihood of Exposure |  |
| Minor | 1 | Highly Unlikely | 1 | Score Rating a) x b) | 0 |